## Slide 1
S a n d i a N a t i o n a l L a b o r a t o r i e s
Mark C. Herrmann
Pulsed Power Sciences Center, Sandia National Laboratories
in collaboration with my colleagues at Sandia National Laboratories
December 5, 2012
Sandia is a multiprogram laboratory operated by Sandia Corporation, a Lockheed Martin Company, for the United States Department of Energy’s National Nuclear Security Administration under contract DE-AC04-94AL85000.
Fusion at Sandia National Laboratories

## Slide 2: Summary
  Pulsed power is an efficient, cost-effective way to create matter at high energy densities
  Magnetically driven implosions offer a path to coupling much higher fractions of the driver stored energy to fusion fuel
  Magnetized Liner Inertial Fusion (MagLIF) offers a near term chance for testing our understanding of magnetically driven implosions.
  Experimental data on the Magneto-Rayleigh Taylor instability is promising, we will begin integrated MagLIF testing in 2013.
  A high-yield (GJs), high-gain (>500) MagLIF design is under development. Much of the relevant physics can be tested on Z.

## Slide 3: Large currents and the corresponding magnetic fields can create and manipulate high energy density(HED) matter
Magnetic fields have some unique advantages when creating HED plasmas:
  Magnetic fields are very efficient at creating HED matter enabling large samples and energetic sources
  Magnetic fields have very interesting properties in converging geometry
Magnetic fields have interesting contrasts with other ways of generating HED:
  Magnetic fields can create high pressures without making material hot
  Magnetic fields can be generated over long time scales with significant control over the time history
Magnetic fields change the way particles and energy are transported in a plasma
HED Matter P > 1 Mbar, B > 5 Megagauss

## Slide 4: We use the Z pulsed power facility to generate large magnetic fields
22 MJ stored energy
3MJ delivered to the load
26 MA peak current
5 – 50 Megagauss (1-100 Megabar)
100-600 ns pulse length
Tank~10,000 ft2

## Slide 5: Magnetically driven implosions can efficiently couple energy at high drive pressure
Magnetic drive can reach very high drive pressures if current reaches small radius
Magnetic drive is very efficient at coupling energy to the load (no energy wasted on ablation)
100 MBar is comparable to drive pressure on a NIF capsule
MBar
R
drive
current
I
Magnetically-Driven Implosion
100 MBar at 26 MA and 1 mm
However cylindrical implosions do not have nearly as high a pressure multiplier on stagnation
Cylindrical shells must be thick to avoid disruption by instabilities
Thick shells are slow, making the pressure problem harder

## Slide 6
Fuel areal density (g/cm2)
Temperature (keV)
*Basko et al. Nuc. Fusion 40, 59 (2000)
The rr needed for ignition can be significantly reduced by the presence of a strong magnetic field
  inhibits electron conduction
  enhances confinement of alpha particles
Lower rr means lower densities are needed (~1 g/cc)
Pressure required for ignition can be significantly reduced to ~5 Gbar
(<< 500 Gbar for hotspot ignition)
Large values of B/r are needed and
therefore large values of B are needed.
B~ 50-150 Megagauss >> B0 -> flux compression is needed
Magnetization significantly reduces the self heating requirements for inertial confinement fusion
Z
goal

## Slide 7
compressed
axial field
3. The Z accelerator can provide the drive current which generates an azimuthal drive field (pressure) to efficiently implode the thick liner at 50-100 km/sec
and compress the axial field to 100 MG
The Z facility provides an opportunity to test the benefits of fuel magnetization and preheat
cold deuterium/tritium
gas (fuel)
Metal (beryllium)
Cylindrical Liner
A 100-500 kG axial magnetic field
is applied before the implosion
laser
beam
Laser
preheated
fuel
2. Z Beamlet can preheat the fuel to ~100 - 1000 eV
to reduce the compression and velocity needed
Simulations indicate fusion energy out = energy deposited in fusion fuel
may be possible on Z
* S. A. Slutz et al., Physics of Plasmas 17, 056303 (2010).

## Slide 8
laser heating: 120-124 ns

## Slide 9
Max Planck / ITEP
Los Alamos / Air Force Research Lab
Field Reversed Configuration
Shiva Star generator
~20 s, 0.5 cm/s liner implosion
U. Rochester LLE
Direct drive laser implosion of cylinders
-- shock pre-heating, high implosion velocity
Sandia National Laboratories
Magnetized Liner Inertial Fusion
Laser preheated magnetized fuel
LASNEX simulations indicate interesting yields
Basko, Kemp, Meyer-ter-Vehn, Nucl. Fusion 40, 59 (2000)
Kemp, Basko, Meyer-ter-Vehn, Nucl. Fusion 43, 16 (2003)
Gotchev et al., Bull. Am. Phys. Soc. 52, 250 (2007)
Gotchev et al., Rev. Sci. Instr. 80, 043504 (2009)
Gotchev et al., Phys. Rev. Lett. 103, 215004 (2009)
Knauer et al., Phys. Plasmas 17, 056318 (2010)
Taccetti, Intrator, Wurden et al., Rev. Sci, Instr. 74, 4314 (2003)
Degnan et al., IEEE Trans. Plas. Sci. 36, 80 (2008)
Bz
Z
ZBL
liner
current
The parameter space for magnetized ICF is large allowing a diverse set of approaches
S. A. Slutz et al., Phys. Plasmas, 17, 056303 (2010).
D.B. Sinars et al., Phys. Rev. Lett. 105, 185001 (2010)

## Slide 10
Simulations indicate fusion energy out = energy deposited in fusion fuel may be possible on Z with DT fuel
INITIAL CONDITIONS
Peak Current: 27 MA
Be Liner R0: 2.7 mm
Liner height: 5 mm
Aspect ratio (R0/DR): 6
Initial gas fuel density: 3 mg/cc
Initial B-field: 30 T
Preheat Temperature: 250 eV
FINAL CONDITIONS
Energy in Fusion Fuel ~200 kJ
Target Yield: 500 kJ
Convergence ratio (R0/Rf): 23
Final on-axis fuel density: 0.5 g/cc
Peak avg. ion temperature: 8 keV
Final peak B-field: 13500 T
Peak pressure: 3 Gbar
2D yield for a DT target ~ 350 kJ (70% of 1D)
Radius (m)
The magneto-Rayleigh Taylor instability is a big concern for this concept
60 nm surface roughness,
80 (m) waves are resolved

## Slide 11: The lower opacity of beryllium at 6.151 keV allows us to take penetrating radiographs of the liner implosions
High opacity of Al means that we only see the edge of the liner
Lower opacity of Be means that we can see through the liner and the “spikes” show up as dark bands
Machining of beryllium targets is done at General Atomics in La Jolla, CA

## Slide 12: We’ve done stability experiments on Be liners at higher radial convergence
AR=6:
router,0 = 3.47 mm
rinner,0 = 2.89 mm
How does the 2D correlation emerge?

## Slide 13: MagLIF-relevant beryllium liner implosion data was collected and is actively being used to benchmark our modeling tools
R.D. McBride et al., Phys. Rev. Lett. 2012; APS-DPP invited talk in October

## Slide 14
Recent studies examined a thin Al sleeve inside a Be liner to study the integrity of the inner surface

## Slide 15
Recent studies examined a thin Al sleeve inside a Be liner to study the integrity of the inner surface

## Slide 16
Recent studies examined a thin Al sleeve inside a Be liner to study the integrity of the inner surface

## Slide 17
Recent studies examined a thin Al sleeve inside a Be liner to study the integrity of the inner surface

## Slide 18
Recent studies examined a thin Al sleeve inside a Be liner to study the integrity of the inner surface

## Slide 19
Recent Z experiments have examined
how the target compresses
Liner
Initial
Radius
MagLIF Goal
~ 200 microns
(2 human hairs)
Intact
Inner
Surface
Perturbed
Outer Surface
Wall
Successful compression of a MagLIF liner observed to convergence ratio 5

## Slide 20: An 8 mF, 15 kV, 900 kJ capacitor bank is being installed on Z to drive the coils
Two identical units (repurposed from ion beam facilities) allows for high-fidelity surrogacy testing in separate test facility
We believe 900 kJ is enough to meet our short and long term goals (30 T)
Magnetic Coil Testbed (MCTB)
1st 900kJ Capacitor Banks
Surrogate Vacuum Chamber (SVC)
The SITF Testbed in Bldg. 970
Commissioning of coils in the Z chamber to begin in January
D.C. Rovang et al., see http://www.sandia.gov/pulsedpower/maglifpres/Agenda.html
Photo of capacitor bank w/o covers; with covers

## Slide 21: Preheating experiments using the 2w Z Beamlet laser will begin soon
polyimide membrane
gas
2 beam
0.08 ncr
0.12 ncr
0.16 ncr
* N.B. Meezan et al., Phys. Plasmas (2004); ** J.D. Moody et al., Phys. Plasmas (2009).
Prior work* found agreement between experiments and Hydra simulations assuming classical absorption of 2 for ne/ncr ~ 0.05 to 0.15 gasbag targets on the HELEN Laser
Other work** showed efficient coupling of 2 to 0.13ncr gasbag plasmas at intensities <3x1014 W/cm2, even without beam smoothing
Standalone preheat experiments on Z in January using 2 kJ from ZBL will be used to test our HYDRA predictions for the level of plasma heating. We are also looking at the possibility of OMEGA experiments to study plasma lifetimes in the presence of a magnetic field.

## Slide 22: Next Steps for MagLIF concept
Initial experiments with an external magnetic field are scheduled for February, 2013.
Laser preheat experiments will also be performed in February, 2013.
Initial integrated experiments with both laser preheat and Bz will be performed next July.
Integrated experiments with full capability (laser and Bz) will take place in CY14/15.
If successful we will examine what it would take to pursue experiments with Tritium.

## Slide 23: Calculations indicate yields > 1GJ are possible with MagLIF targets at currents of 60 MA
heated gas
Cryogenic DT
Metal liner
Laser beam
Radius
Axial distance
BQ
Drive current
unheated gas
Yield (MJ/cm) or Gain
Peak current (MA)
Al with cryo
Be with cryo
Be no cryo
*S.A. Slutz and R.A. Vesey Physical Review Letters 108, 025003 (2012)

## Slide 24: The Linear Transformer Driver (LTD) is the most fundamental advance in pulsed power since the invention of the Marx generator in 1924
An LTD Cavity is the building block of SPARC
SPARC-Z= 5400 cavities
An LTD consists of :
Capacitors
Switches
Magnetic cores

## Slide 25: SPARC-Z would be an 800-TW, 63MA, 50 m diameter pulsed-power accelerator.
water-insulated radial-transmission-line impedance transformers
magnetically insulated transmission lines (MITLs)
linear-transformer-driver (LTD) modules (90 total)
vacuum-insulator stack
Eg = 130 MJ
Pg = 830 TW
Vstack = 16 MV
Iload = 63 MA
implosion = 110 ns
Eradiated = 20 MJ
Lvacuum = 20 nH
diameter = 50 m
= 15%
Notes: Minor changes to the references.

## Slide 26
A fully automated proof-of-principle facility provides the first test of defined RTL requirements
Fully engineered prototype facility
  ~10 second cycle time
  >10,000 cycles
Compatible with IFE facility concept
  MITL vacuum/power-flow continuity
  Pre-pumped MITLs
  Extended transmission lines or fast
  closure valves for high-yield standoff
Small-scale (~1/5) prototype
  Ease of maintenance
  Rapid modifications and retrofits
Compatible with LTD architecture
  High-rep-rate pulsed power testing
  Repetitive electrode conditioning studies; increased efficiency

## Slide 27: Summary
  Pulsed power is an efficient, cost-effective way to create matter at high energy densities
  Magnetically driven implosions offer a path to coupling much higher fractions of the driver stored energy to fusion fuel
  Magnetized Liner Inertial Fusion (MagLIF) offers a near term chance for testing our understanding of magnetically driven implosions.
  Experimental data on the Magneto-Rayleigh Taylor instability is promising, we hope to begin integrated MagLIF testing in 2012.
  A high-yield (GJs), high-gain (>500) MagLIF design is under development. Much of the relevant physics can be tested on Z.