## Slide 1: Current Status of IFMIF
Yoshikazu OKUMURA
Deputy Project Leader, IFMIF/EVEDA
FUSION POWER ASSOCIATES, 35th Annual Meeting and Symposium December 16-17, 2014

## Slide 2: What is IFMIF/EVEDA?
IFMIF
International Fusion Materials Irradiation Facility
EVEDA
Engineering Validation & Engineering Design Activities
Article 1.1 of Annex A of the Broader Approach (BA) Agreement
mandates IFMIF/EVEDA
…to produce an integrated engineering design of IFMIF and the data necessary for future decisions on the construction, operation, exploitation and decommissioning of IFMIF, and to validate continuous and stable operation of each IFMIF subsystem
Signed in February 2007
Entered into force in June 2007

## Slide 3: IFMIF through all technical steps
IFMIF
has successfully passed through all needed key steps
Conceptual Design Activity (CDA) phase in 1995-1997
as a joint effort of the EU, Japan, RF and US
Conceptual Design Evaluation (CDE) report in 1998
towards a design simplification and cost reduction
Comprehensive Design Report (CDR) in 2004
co-written by a committee of EU, Japan, RF, US

## Slide 4: IFMIF/EVEDA Project under BA Activities
Since 2007, IFMIF/EVEDA (Engineering Validation and Engineering Design Activities) under the Broader Approach Agreement between EU and Japan
Validation Activities: 1. Accelerator Facility
2.Target facility
3. Test Facility
7 countries involved
with the respective main research labs in Europe
and main labs and universities in Japan

## Slide 5: Engineering Design of IFMIF 2013
IFMIF Intermediate Engineering Design report
was successfully accomplished

## Slide 6: IFMIF Concept
L
M
H
Test Cell
High (>20 dpa/y, 0.5 L)
Medium (>1 dpa/y, 6 L)
Low (<1 dpa/y, > 8 L)
Accelerator (125 mA x 2)
100 keV 5 MeV 9 14.5 26 40 MeV
HEBT
Injector
140 mA D+
LEBT
RFQ
MEBT
RF Power System
Half Wave Resonator Superconducting Linac
Beam shape:
200 x 50 mm2
Lithium Target
25±1 mm thick, 15 m/s
Engineering Validation IFMIF/EVEDA in BA
Engineering Validation IFMIF/EVEDA in BA
IFMIF is an accelerator based neutron source using Li(d,n) reactions aiming at providing a material irradiation database for the design, construction, licensing, and safe operation of DEMO.
IFMIF consists of two deuteron linear accelerators, free surface liquid lithium target, test cell, and the post irradiation examination facility.

## Slide 7: IFMIF/EVEDA Project in Rokkasho
★
Rokkasho
IFMIF/EVEDA Accelerator
Building (for LIPAc)
Cafeteria
DEMO R&D Building
Administration & Research Building
Computer Simulation & Remote Experimentaion Building
A new research center was established in Rokkasho for Broader Approach activities in 2007.

## Slide 8: Linear IFMIF Prototype Accelerator (LIPAc)
8
Injector（100keV）
Radio Frequency Quadropole
（RFQ)(0.1MeV-5MeV)
Super-Conduction Linac (5MeV-9MeV)
Building, Auxiliary
System, Control
Beam Dump
(1.1MW/CW)
RF Power Supply

## Slide 9: LIPAc installation in Rokkasho
Injector has been installed in Rokkasho and commissioning started.
Requirements | Target value
Particles | D+
Output energy | 100 keV
Output D+ current | 140 mA
D+ fraction | 95 %
Beam current noise | 1 % rms
Normalized rms transverse emittance | 0.25 π.mm.mrad
Duty factor | CW
Beam turn-off time | < 10 µs

## Slide 10: LIPAc First Beam
The first beam was obtained on 4th November 2014, under the collaboration with EU and Japan

## Slide 11: Injector Commissioning
Reached to 100keV/105mA 0.5s 50%duty on 6th Nov.
Demonstrated 100% duty operation at 100keV/70mA on 12th Dec.
Considering the aperture diameter of 8mm in the plasma electrode, we can expect more than 100mA D+ with 12 mm diam. aperture.

## Slide 12: RFQ will be delivered in spring 2015 2015
175 MHz; Iinput= 130 mA ; Eoutput= 5 MeV
Up to 10mA beam losses allowed
Max surface field 25.2 MV/m (1.8 Kp)
Fabrication of RFQ is almost completed in INFN, Italy.
Delivery to Rokkasho scheduled in spring 2015
9.85 m long

## Slide 13: RF Modules are ready for shipping
RF Power Supply (CIEMAT, Spain)

## Slide 14: Linac and B.D. are under fabrication
Superconducting HWR resonator at 175 MHz
Einput= 5 MeV
Eoutput= 9 MeV
Beam loss < 10W
Eacc=4.5 MeV/m
Max transm. RF power = 70 kW
9MeV, 125mA, (1.13MW) CW
Radiation Shielding
Superconducting Linac (CEA, Saclay)
Beam Dump (CIEMAT, Spain)

## Slide 15: Lithium Target Facility
World largest liquid Li loop
constructed by
JAEA in Oarai
Built in Nov 2010
Started operation in March 2011
★
★
Rokkasho
Oarai
Target Assembly
(in a enclosure)
20 m
Vacuum pumps
Li Sampling system
Electromagnetic pumps (3000 l/min)
Li dump tank

## Slide 16
Long term operation stability
(>1000 hours)
demonstrated
Target Facility Validation main achievements
Operation conditions of the IFMIF;
Temperature: 250 ℃ Vacuum: 10-3 ~ 10-2 Pa
Li flow rate: 15 m/s
has been achieved.
Completed its operation in October 2014

## Slide 17: IFMIF Test Facility
High >20 dpa/y, 0.5 liters
Medium >1 dpa/y, 6 liters
Low <1 dpa/y, 8 liters
TEST CELL
HFTM
MFTM
LFTM

## Slide 18
12 capsules within beam footprint
x2 sets of 40-45 spec/set
within 3% ΔT/capsule
80-90 specimens/capsule
Validation of High Flux Test Module
Specimen filling in hot cell
Handling of specimens in hot cell demonstrated

## Slide 19
Capsules of HFTM
have successfully entered
a nuclear reactor environment
Stack assembly (unirradiated specimens)
validated in Hot Cell environment
Small Specimens shape defined
for a full characterization of RAFM
Successful cooling with He gas of capsules
reaching ΔT within 3% gradient per capsule
Understanding behaviour of
capsule heaters and thermocouples
under irradiation conditions
On-going
Test Facility Validation Achievements

## Slide 20: IFMIF/EVEDA Global Schedule
SYSTEM DESIGN, FABRICATION,TEST & DELIVERY
Accelerator Facility
COMMISSIONING
INJECTOR & LEBT
RFQ
SRF Linac.
Target Facility
SYSTEM DESIGN, FABRICATION & COMMISSIONING
Test Facility
SYSTEMS DESIGN; FABRICATION; COMMISSIONING & TESTING
Start
PHASE I
PHASE II
PHASE III
IIEDR Final
Delivery.
Syst.
DDD-I
Syst.
DDD-II
IFMIF ENGINEERING DESIGN ACTIVITIES
HELOKA-LP
Commissioned
HFTM-SR
Manuf. & Tested
End of HFTM-V (Europe)
Validation Activities
BR2 Irradiation
Completed
2nd Cycle
3rd Cycle
End of HFTM-H (Japan)
Validation Activities
EXPERIMENT