## Slide 1: Laying the foundational technology for IFE laser drivers Fusion Power Associates Meeting December 16, 2014
Tom Anklam
NIF&PS Deputy Associate Director for S&T

## Slide 2: Feasibility and Technology Challenges for IFE
Demonstrate ignition
Design and demonstrate a laser driver
Address issues affecting availability such as optical damage
Target mass manufacturing, injection, tracking, engagement
Fusion chamber design, materials of construction, durability issues
Closing the tritium fuel cycle
Economics
Laser drivers also have scientific and commericial applications

## Slide 3: IFE laser attributes – indirect drive
High electrical efficiency
MJ – class energy level
10 Hz to 20 Hz repetition rate
Steering capability to engage moving targets, compensate for vibration
Optical damage resistant at billion-shot level
High system availability
Appropriate form factor for production environment
Designed for manufacturability and cost effectiveness

## Slide 4: LLNL design combines the NIF architecture with high efficiency, high average power technology
16 J/cm2 1w
4.7 J/cm2 3w
Rotator
l/4
Diodes
Diodes
Diode pumps  high efficiency (18%)
Helium cooled amps  high repetition rate (16 Hz) with low stress
Normal amp slabs  compensated thermal birefringence, compact amp
Passive switching  performs at repetition rate
Lower output fluence  less susceptible to optical damage

## Slide 5: An entire 1w beamline that provides 130 kW average power can be packaged into a 31 m3 box
10.5 m
1.35 m
2.2 m
Diode array
Pockels cell
Amplifier head
Preamplifier module (PAM)
Deformable Mirror
NIF Beam Line Capability in a Very Small Box

## Slide 6: The LLNL laser design is projected to achieve high efficiency
Chart: Diode Power (MW)
| 40.076792206313023 | 49.460649164012004 | 60.387130206551312 | 68.94872640213552 | 81.715226713043506
 | 16.7214 | 18.483 | 19.7238 | 20.3287 | 21.0217
 | 15.0643 | 16.6514 | 17.7692 | 18.3142 | 18.9384
 | 18.5608 | 20.5162 | 21.8934 | 22.5649 | 23.334
223 ms
164 ms
125 ms
106 ms
Pump pulselength
Electrical to 3w Optical Efficiency
variability
Laser point
Design
83 ms
Capital Cost →
78 104 130 156 182 208 234
APG-1 laser glass
5.7 kJ/beam @ 3w
25-cm aperture @ 1w
1-cm-thick slabs
Cooling power not included
(~16% including cooling)

## Slide 7: LLNL average power lasers have been proving grounds for several key proposed laser technologies
25 kW high average power laser
AVLIS 24/7 operational laser
600W, 10 Hz Mercury Laser
300 Hz, 38 W Pulse Amplifier

## Slide 8: High availability using hot-swappable components was demonstrated on AVLIS
AVLIS maintained long-term (10 year) 24/7 operation at 99% availability
with 1500 hr MTBF line replaceable units (LRUs)

## Slide 9
HAPLS project:
Delivery of a laser system for a 10 Hz, 1 Petawatt user facility, incorporating a 200 J / 10 Hz DPSSL pump laser
LLNL diode-pumped laser technology is being integrated into the “ELI Beam lines” facility in Europe

## Slide 11: GOLD Laser System is being developed to test optical damage at the gigashot level
100 Hz, 10J
7mm x 7mm beam footprint
20J/cm2 red, 12J/cm2 blue
First light end of FY15
DPSSL performance to exceed kW

## Slide 12: GOLD and ELI are driving demonstration of increasingly capable diode arrays
GOLD: 120 Hz, 126 kW
ELI L3: 10 Hz, 800 kW

## Slide 13: 800 kW QCW diode array in action at 10 Hz
800 kW peak @ 120 Hz
2.4 kW average power

## Slide 14: Near-term laser development for scientific and commercial application also advances that needed for IFE
Diode pumps  high efficiency (18%)
Helium cooled amps  high repetition rate with low stress
Normal amp slabs  compensated thermal birefringence,
Passive switching  performs at repetition rate
Lower output fluence  less susceptible to optical damage

## Slide 16: Optics durability will be key
GOLD System under construction – giga-shot, multi-year test campaign
120 Hz, >10 J operation
Low fluence design – providing a robust source to test optics under LIFE-relevant conditions
Of immediate-term application to facilities such as ELI
100 Hz amplifier front-end
DPSSL performance to exceed kW

## Slide 17: NIF beamline capability in a very small box: Proposed high average power laser architecture attributes
Provides efficiency (~18%) at high repetition rate (16 Hz)
  High brightness efficiency diode pump arrays
  Helium gas-cooled amplifiers
  High harmonic conversion efficiency
Designed to be built with existing materials
  Glass slabs: thermal birefringence compensated by architecture
  DKDP Pockels cell: passive polarization switching minimizes heat load
Designed for high reliability and low operating costs
  Low 3w fluence operation
  Margin in beamline power
  Optics preparation to mitigate damage effects
Designed with modular beamlines in clean protective boxes that can be transported
  Maintenance can be performed by removal and replacement of beamlines
  Assembly can be performed at factories rather than at the laser operating site

## Slide 18: Architecture has previously been used to demonstrate high availability and maintainability
Beam-in-a-Box

## Slide 20
the proposed design,

## Slide 21: HAPLS leverages many elements of the LIFE design scaled down from multi-kJ operation
Rotator
l/4
Diodes
Diodes
Diode pumps  high efficiency
Helium cooled amps  high repetition rate with low stress
Normal amp slabs  compensated thermal birefringence, compact amp
Passive switching  performs at repetition rate
Lower output fluence  less susceptible to optical damage