## Slide 1: Fast Ignition Inertial Confinement Fusion
Pravesh Patel
Fusion Power Associates
32nd Annual Meeting and Symposium
Washington D.C.
December 14-15, 2011
Associate Program Leader for Fast Ignition

## Slide 2: Fast Ignition is an ICF scheme that has the potential for high gain by decoupling fuel compression and heating
Large fuel mass can be compressed with low velocity, low convergence implosion ⇒ high gain (>100)
Conventional implosion compresses DT fuel:
~ 300 g/cm3
R ~ 2 g/cm2
Intense laser-generated electron beam rapidly heats core to 10 keV:
Eign ~ 10 kJ
P ~ 0.5 PW
I ~ 1020 W/cm2
The new challenge FI introduces is to create the required electron flux and couple it efficiently to the dense core to achieve ignition

## Slide 3: There is a large active research community studying Fast Ignition HED Science – at national & international level
University of Rochester
General Atomics
UCLA
MIT
UCSD
Ohio State University
University of Nevada
University of Texas
ILSA
LLNL
Ion/Proton FI
HEDLP
Electron FI
This work is supported by the OFES-NNSA Joint Program in High-Energy-Density Laboratory Plasmas
Notes: FI challenge has generated research interest across universities and national labs across the world.
In the last couple of years we have seen a new level of co-ordination at national and international levels

## Slide 4: Two major facilities are performing integrated core heating experiments to test FI physics, at ~0.01 to 0.1 ignition scale
Gekko XII laser facility, Japan
2.5 kJ 9 beam compression + 400 J heating
Demonstrated core heating of rR≈<0.1 g/cm2 core
OMEGA laser facility, US
20 kJ 48 beam compression + 1 kJ heating
Demonstrated core heating of rR≈0.3 g/cm2 core
Kodama et al. (2003)
Theobald et al. (2011)

## Slide 5: We are able to leverage newly emerging laser facilities to test all of the key physics of fast ignition
LULI 100TW
Vulcan TAW
Helen
Trident
Texas
Vulcan PW
LULI 2000
TITAN
10J
100J
1kJ
10kJ
100kJ
1MJ
10MJ
10J
100J
1kJ
10kJ
100kJ
Long Pulse Energy
Short Pulse Energy
Gekko XII
Pre-2009

## Slide 6: We are able to leverage newly emerging laser facilities to test all of the key physics of fast ignition
LULI 100TW
Vulcan TAW
Helen
Trident
Texas
Vulcan PW
LULI 2000
TITAN
10J
100J
1kJ
10kJ
100kJ
1MJ
10MJ
10J
100J
1kJ
10kJ
100kJ
Long Pulse Energy
Short Pulse Energy
High Gain FI
Gekko XII
Pre-2009

## Slide 7: We are able to leverage newly emerging laser facilities to test all of the key physics of fast ignition
LULI 100TW
Vulcan TAW
Helen
Trident
Texas
Vulcan PW
LULI 2000
TITAN
OMEGA EP
10J
100J
1kJ
10kJ
100kJ
1MJ
10MJ
10J
100J
1kJ
10kJ
100kJ
Long Pulse Energy
Short Pulse Energy
High Gain FI
Gekko XII
Pre-2009
2009+

## Slide 8: We are able to leverage newly emerging laser facilities to test all of the key physics of fast ignition
LULI 100TW
Vulcan TAW
Helen
Trident
Texas
Vulcan PW
LULI 2000
TITAN
Gekko+LFEX (2012)
NIF+ARC (2012)
OMEGA EP
10J
100J
1kJ
10kJ
100kJ
1MJ
10MJ
10J
100J
1kJ
10kJ
100kJ
Long Pulse Energy
Short Pulse Energy
High Gain FI
LMJ+PETAL (2015)
ORION (2012)
To establish the feasibility and energy requirements for FI we need an integrated target design, or point design, at high gain
Gekko XII
Pre-2009
2009+

## Slide 9: Integrated modeling of FI is challenging due to the multi-scale physics inherent in short & long-pulse interactions
We began a program to develop a predictive integrated simulation capability for FI (intense laser interaction with HED plasma)

## Slide 10
We have designed NIF-compatible cone-in-shell implosions that if ignited can release 150 MJ fusion yield
1.4 MJ laser drive
Yield =150 MJ
Gain ~100 (without ignitor energy)

## Slide 11: To model the ignitor pulse we have performed 3D PIC simulations of a 1.3 PW pulse at full spatial scale
ne/nc
Laser
Electron flux 50-75% – higher than previously assumed
Mean energy (1.4x theory), divergence (35-50˚) – higher than assumed
3D cartesian simulation (60 kcpu-hrs)
1.4x1020 W/cm2, 40 µm spot, 1 ps
PSC-hybrid† simulation of ignition pulse
Parameterized as functions of energy, angle, radius, time – dN/d(E, q, r, t)
Fast electron source distribution
†B.I. Cohen et al., J. Comp. Phys. 229, 4591 (2010); A.J. Kemp et al., Phys. Plas. 17, 056702 (2010)

## Slide 12: The PIC source is injected into integrated simulations of fast electron transport, heating, and burn
PIC-source (Dq=90˚)
Artificially collimated (Dq=10˚)
full yield (64 MJ)
Predicted electron divergence is the most crucial parameter
— is it right?
— can we use new target designs to improve coupling?

## Slide 13: Understanding the properties of laser absorption, electron generation and transport is our fundamental challenge
In 2D we can now run full spatial scale simulations to >5 ps (300 kcpu-hrs, 1-wk on 2000 cpus)
Simulations of laser-matter interaction at FI-scale test the limits of current computational capabilities
Electron generation & transport are highly coupled processes
Independent code predictions do not presently agree
Experimental validation is absolutely critical

## Slide 14: Understanding the properties of laser absorption, electron generation and transport is our fundamental challenge
Simulations of laser-matter interaction at FI-scale test the limits of current computational capabilities
Electron generation & transport are highly coupled processes
Independent code predictions do not presently agree
Experimental validation is absolutely critical
Electrons
Laser
Electrons
PSC-Hybrid
ZUMA+HYDRA
Giga-Ampere current flowing into dense plasma induces response through return current, electric, magnetic fields
We are developing a self-consistent framework

## Slide 15: Understanding the properties of laser absorption, electron generation and transport is our fundamental challenge
Kemp, Strozzi (LLNL)
Chrisman (UNR)
Debayle (U. Madrid)
Fiuza (IST, Portugal/UCLA)
We initiated code comparison workshops (2009, 2010 at LLNL) bringing together >30 FI modelers across US, Europe, and Japan
Helped to reveal and assess uncertainties
Simulations of laser-matter interaction at FI-scale test the limits of current computational capabilities
Electron generation & transport are highly coupled processes
Independent code predictions do not presently agree
Experimental validation is absolutely critical

## Slide 16: Understanding the properties of laser absorption, electron generation and transport is our fundamental challenge
Data
Simulation
Target
ncrit
TITAN laser
1020 W/cm2
Reflected light
v/c
red-shift
blue-shift
PIC simulation of TITAN laser interaction with solid target
450 kcpu-h run at full spatial and temporal scale
Electrons
Laser
Experiments on Titan laser (LLNL) & Omega (LLE) are now providing high quality data to validate simulations and understanding
Simulations of laser-matter interaction at FI-scale test the limits of current computational capabilities
Electron generation & transport are highly coupled processes
Independent code predictions do not presently agree
Experimental validation is absolutely critical

## Slide 17: As we gain understanding of the electron source we can use target design to optimize coupling to core (maximise gain)
A resistivity gradient created by two layers of different materials can generate a multi-MG field through (∇h)×jf
Resitively generated magnetic field
Au/Cu/Au multilayers
Magnetic flux compression of a seed field has been demonstrated at LLE
A hollow axial field ~50MG can efficiently guide electrons to core
Flux compression of a seed field
No
B-field
Compressed B-field
Electron current

## Slide 18: Advances in simulation capability are now enabling us to develop FI designs in an integrated, self-consistent manner
We are close to being able to model and study the ignitor laser interaction at full spatial and temporal scale
The self-consistent treatment of electron generation and transport is currently the area of greatest uncertainty
Experiments on current generation facilities are playing a critical role in validating these simulation tools
We expect to develop a robust point design that serves as the basis for high gain fast ignition demonstration

## Slide 19
Backup Slides

## Slide 20: We are now doing larger scale simulations and developing methodology to inject to Zuma, Hydra

## Slide 21: We are now studying the surrogacy between ignition-scale and Titan-scale laser-plasma interaction
Ignition-scale
Titan-scale
f/20 focusing
40 µm wide uniform spot
20 ps pulse duration
f/3 focusing
5 µm wide Gaussian spot
0.5 ps pulse (typically)
Critical question: Is the dominant physics the same in both cases?

## Slide 22: Understanding the properties of laser absorption, electron generation and transport is the fundamental challenge
In 2D we can now run full spatial scale simulations to >5 ps (300 kcpu-hrs, 1-wk on 2000 cpus)
Simulations of laser-matter interaction at FI-scale test the limits of current computational capabilities
Electron generation & transport are highly coupled processes
Independent code predictions do not presently agree
Experimental validation is absolutely critical

## Slide 23: To model electron transport and burn we have linked the ZUMA hybrid-PIC code with the HYDRA code
HYDRA:
3-D multiphysics radiation-hydrodynamics ICF code
Two codes run in parallel: dissimilar domains, meshes, and timesteops
Energy, momentum deposition rates and magnetic fields exchanged
ZUMA:
3-D hybrid-PIC relativistic electron transport code
Test case: 3-D relativistic electron beam injected into 50 g/cc DT plasma
Magnetic field
Plasma temperature

## Slide 24: Since the first ignition calculations we have studied the electron source in more detail
    I. Source is not really separable into f(E,q,y) = fE(E) × fq(q) × fy(y)
  Electrons in centre of beam, and electrons with higher energy have smaller divergence
  We are now putting full source distribution into ignition calc.
    II. Simulation is short in time (365 fs)
  We have performed longer duration, full spatial-scale, 2D PIC simulations (> 5ps)
  We have compared with reduced scale 3D PIC simulations

## Slide 25
PIC simulations need to be validated by experiment
Target
v/c
Critical density surface
Titan laser
1020 W/cm2, 1.4 ps
Reflected light
red-shift
blue-shift
Data
Simulation
2-D PIC sumulation of Titan laser pulse (full spatial/temporal scale)
Agreement is only achieved by inlcuding relativistic self-focusing/filamentation in the preplasma, and accurate modeling of plasma heating (to get right back-pressure)
fast electrons

## Slide 26: Next step is to study electron distribution and compare with data (Ka and bremsstrahlung)
Electrons fluctuate rapidly in time – important for time-integrated data
We are coupling electron distribution to ZUMA to compare with data