## Slide 1
Status of US Contributions
to the ITER Project
Ned Sauthoff
US ITER Project Manager
Oak Ridge National Laboratory
Fusion Power Associates 33rd Annual Meeting
6 December, 2012
Washington, DC

## Slide 2: Contents
Status of US Industrial Contributions
Magnets & Superconductors
Cooling Water System
Vacuum and Exhaust Processing
Electron and Ion Cyclotron Heating
Steady State Electrical Network
Diagnostics
Pellet Injection
Plasma Disruption Mitigation

## Slide 3: US Scope is Managed by ORNL in partnership with PPPL, SRNL and US Industry
ORNL
100% Central Solenoid
Windings
+ JA Support
ORNL
8% of Toroidal
Field Conductor
+ JA Support
ORNL
100% Pellet Injector
100% Disruption Mitigation
ORNL
Blanket/Shield
(design only)
ORNL
100% Tokamak Cooling Water System
PPPL
75% Steady State
Electrical Network
PPPL
14% of Port-based
Diagnostics
ORNL
88% Ion Cyclotron
Transmission Lines
ORNL
88% Electron
Cyclotron
Transmission Lines
PPPL
In-Vessel Coils
(prelim. design only)
ORNL
100% Roughing Pumps,
Vacuum Standard Components
SRNL
100% Tokamak Exhaust
Processing System
SCALE

## Slide 4
US Hardware is Highly Integrated
with the Tokamak Core
Cooling Water System (TCWS)
ICH Transmission System
ECH Transmission System
Vacuum Auxiliary System (VAS)
Port Diagnostics
Central Solenoid (CS) Coil
Toroidal Field (TF) Coil (1)
Blanket/Shield (design only)
Pellet Injection (PI) &
Disruption Mitigation (DM)
Not Shown:
Roughing Pump System (RPS)
Steady-State Electrical Network
(SSEN)
Tokamak Exhaust Processing
(TEP)

## Slide 5
US Scope is Delivered in Two Phases
First Plasma
Post-First Plasma
Designs
CS Coil & TF Conductor,
TCWS, VAS/RPS, TEP, SSEN
Diagnostics
PI & DM
Design Support
In-vessel coils
Blankets/shields
Production Completion
ICH/ECH
TCWS
VAS
Full Production
TEP
Diagnostics
Full Production
CS Coil & TF Conductor,
RPS, SSEN
Partial Production
ICH/ECH, TCWS, VAS
All designs completed
during Pre-First Plasma
phase.

## Slide 6
From developing requirements to completing designs
From R&D to large-scale prototypes
From prototypes to large-scale manufacturing
To fabrication
Transitioning from
Design to Fabrication

## Slide 7
Critical pacing items currently in fabrication
Toroidal field conductor
Drain tanks for tokamak cooling water system
Over 75 hardware prototypes under development & testing.
7
US Progress is Aligned
with International Partners
First shipments of US hardware to ITER site are already underway (vacuum test equipment)

## Slide 8
Over 80% of Project Funding
is Being Spent in the US
Industries, Universities, and National Laboratories Obligations
Total = ~$446M
Data accurate through September 30, 2012

## Slide 9: Central Solenoid Coil
13 Tesla
7 GJ
20 kV
1.2 T/s
Notes: U.S. supplies 40 tons of Niobium-tin superconducting wire

## Slide 10: Central Solenoid Assemblies
JA-Supplied Conductor
Integrated
CS Stack
6 CS Coil
Modules
(+ one spare)
JA CS Conductor Prototype

## Slide 11
Central Solenoid Forging Prototypes
Welded Tie Plate Fabrication, Major Tool & Machine, Inc., Indianapolis, IN and Scot Forge, Spring Grove, IL.
One Piece Tie Plate Fabrication, G&G Steel, Russelville, AL and Kind LLC, Gummersbach, Germany

## Slide 12
Photo: General Atomics, San Diego, CA
Central Solenoid Module
Fabrication Process at General Atomics
Preliminary Design Review held in Sept 2011 and R&D effort nearly complete
Contract for CS Module Fabrication awarded to General Atomics (GA) in July 2011
Fabrication of Production Module to begin in FY 2014
Module Manufacturing Facility in Poway, CA

## Slide 13: Toroidal Field Coil
11.8 Tesla
41 GJ
400 MN centering force
Notes: U.S. supplies 40 tons of Niobium-tin superconducting wire

## Slide 14: New US Production Scale for Nb3SN
Notes: Images: TCWS design and Stainless steel for drain tank fabrication being prepared for rolling at Joseph Oat Corporation in Camden, NJ.

## Slide 15
Oxford Superconducting Technology
– In Production
  Oxford is now supplying EU with toroidal field strand.
Photos: Oxford Superconducting Technology, Carteret, NJ
Completed all superconducting strand production included in
base awards. Additional strand being fabricated.
Photos: Oxford Superconducting Technology, Carteret, NJ

## Slide 16
Luvata Waterbury – In Production
  Luvata is now supplying Korea with copper strand.
Completed all superconducting strand production included in
base awards.
Photos: Luvata Waterbury, Inc., Waterbury, CT
Luvata Waterbury Inc. Assembled superconductor rods being drawn on their 400-ft long draw bench

## Slide 17
New England Wire Technologies Cable In Production
Completed refurbishment of 4th and 5th stage cabler and successfully cabled 770 m dummy conductor in June 2012.
Tubular cabler in production (Photo: NEWT, Lisbon, NH)
Planetary cabler into forming die (Photo: NEWT, Lisbon, NH)

## Slide 18
High Performance Magnetics – Production of Jacketed Conductor
Tube shipments in stored south warehouse (photo courtesy HPM, Tallahasse, FL)
  All tube shipments received.
Production tooling: cable payoff and straightening machines (photo courtesy HPM, Tallahasse, FL)
  New company formed to integrate cable-in-conduit for final jacketed superconductor.

## Slide 19
19
Tokamak Cooling Water System
Removes ~1 GW of heat
Plasma operations – 880 MW
Neutral Beam Injector (NBI): 85 MW
Vacuum Vessel (VV): 10 MW
Multiple functions
Water and gas baking
Plasma and decay heat removal
Confinement
Design nearing completion
~33,000 meters of pipe
Thermo-hydraulics well understood
System optimization underway

## Slide 20: AREVA/Joseph Oat Corp - Entering Fabrication
Basic Ordering Agreement with AREVA Federal Services
Contract to AREVA/Joseph Oat Placed for Drain Tank Fabrication (September 2011)
Stainless steel plates produced for drain tank heads (March–July 2012)
Manufacturing process readiness review for drain tanks concluded (August 2012)
Final Design Review for full TCWS (February 2014)
Delivery of drain tanks scheduled in FY 14

## Slide 21: Vacuum Auxiliary and Roughing Pump Systems
Vacuum Auxiliary System
(service vacuum for ~5000 clients)
Roughing Pump System
(continuous H, D, T and He gas pumping)
Tritium-Compatible
Roots and Screw
Vacuum Roughing Pumps
Cryogenic Viscous Compressor Vacuum
Pumps
Design mods complete
Procurement underway
Computer model complete
Prototype design complete
Fabrication awarded

## Slide 22: Ion Cyclotron and Electron Cyclotron Heating Systems
Ion Cyclotron Heating
Load-tolerant tuning over 40-55 MHz.
6 MWs/line for pulse lengths up to 3600s.
Electron Cyclotron Heating
Low-loss transmission at 170 GHz.
2 MWs/line for pulse lengths up to 3600s.

## Slide 23: Ion Cyclotron Heating
Technical Challenge:
Delivering up to 6 MW per transmission line for 3600 seconds
Solution:
Coaxial turbulent heat exchange
3 atm air circulating between water-cooled outer conductor and inner conductor
Risk Mitigation:
Develop multiple designs and prototypes
Test to prove performance
ICH transmission line test stand has operated at > 6 MWs for 120 seconds

## Slide 24: Three Types of Gas Barriers are being Tested
SPX – Dielectric (Maine)
Mega Industries (Maine)
General Atomics
(California)
Edge-cooled aluminum nitride ceramic barrier
Gas-cooled quartz barriers

## Slide 25
Electron Cyclotron Heating
Waveguide Switches
Miter Bend
140° Miter bend
CPI Gyrotron
DC Break
Polarizing Miter Bends
Preliminary design phase complete
Prototype fabrication and testing underway

## Slide 26: Steady State Electrical Network
Supplies electrical power to all conventional loads in the ITER facility.
Final design complete (EU).
- US will deliver 75% of equipment (EU 25%).
Procurement authorization in place.
Prionnet 400 KV substation at ITER site already completed and energized.

## Slide 27: Diagnostics & Port Plugs Design Underway
Low Field Side Reflectometer
Design/R&D Contract to be Awarded Jan 2013
Additional Diagnostics Post 1st Plasma with Preliminary Designs Underway
Upper IR/Visible Cameras
Motional Stark Effect
Electron Cyclotron Emission
Toroidal Interferometer/Polarimeter
Core Imaging X-Ray Spectrometer
Port Plugs
Preliminary Designs to be Completed 2013/2014
Residual Gas Analyzer
Preliminary Design to be Completed Jul 2013

## Slide 28
Pellet Injection Component Prototypes in Testing
Twin-screw extruder prototype for hydrogen isotope ice pellet formation.
R&D and Conceptual Design to develop
    20 Hz D/T fueling capability
    30 Hz ELM pacing capability
    Impurity pellet injection
Pellet Injector
Sub-Assembly Design

## Slide 29
Plasma Disruption Mitigation
Methods in Testing at General Atomics
Massive Pellet Injection
Massive Gas Injection
Thermal quench (TQ) and current quench (CQ) test results from DIII-D (Photos courtesy GA).
Toroidal asymmetries indicate non-uniform wall irradiation and thus the need for multiple injection ports.

## Slide 30
Continuing transition from design to procurement and fabrication.
Technical challenges are largely solved, moving to manufacturing.
US industry is engaged, and US technology is advancing.
New US Industrial Capacity is Engaged and Growing

## Slide 31: What ITER Means for the US
Provides the opportunity to create, understand, and control a reactor-size burning plasma.
Demonstrates the scientific and technological feasibility of a promising, virtually inexhaustible and relatively clean energy source.
Positions the US to provide fusion-reactor technology.
Creates high-tech jobs and economic growth in the US.
Notes: Science of “Burning Plasmas”:
The next major step:
Create, understand, and contrdol a reactor-prototypical fusion plasma
  New dynamics of self-heating
  Size-scaling of phenomena at reactor scale
  Effects of “faster-than-light” particles
International partnership
  Refine a model international partnership on large science projects
Improve understanding and effective joint-work between ITER partiesDemonstrate the scientific and technological feasibility of an energy source with
  Virtually-unlimited geographically-dispersed fuel
  No CO2 or acid-rain gases
  No high-level-radioactive waste
  A relatively small scale up in various engineering parameters to a Fusion Demonstration Power Plant
  200 GJ of fusion energy per pulse
Position the U.S. to provide fusion-reactor technology
Create high-tech jobs and work in the U.S.